Tender Specifications AVK Surface box Normpot Brandkraan HD-GG [80/44-006]

1. Range

Normpot Brandkraan / fixed height 200 mm / PA+

2. Product description

General

The surface box shall be for installation in roads, sidewalks or green zones to provide access to underground hydrants.

Basic design

The surface box design shall correspond with AVK surface box Normpot Brandkraan HD-GG series 80 type 44 variant 006 (STV 80/44-006) or equivalent.

Product shall be a heat resistant, synthetic surface box with a ductile iron GJS-500-7 lid attached to the housing by a stainless steel A2-70 bolt with locking clip.

Housing shall consist of one part made out of heat resistant PA+ material.

Upper shape of housing shall be rectangular.

Features

Surface box shall have a max. total weight of 10 Kg.

Housing shall be 100% corrosion-free.

Housing and lid shall be designed to ensure easy opening at all times

Surface box housing and lid shall have a heat resistance of at least 250 °C.

Surface box shall meet D400 load bearing capacity, tested by applying flat load on top surface.

Housing shall be equipped with vertical ribs for optimal fixation in road.

3. Standards and approvals

Surface box shall meet T.V./072/3-E requirements.

4. Sustainability

Surface box shall have a carbon footprint of max. 17 Kg. Carbon footprint (CO2 emission) shall be calculated by using Lifecycle Assessment method according to ISO 14040-44. 
Housing to be made of 100% first grind recycled thermoplastic material.

Housing and lid to be 100% recyclable after end of life.

Surface box shall contain no heavy metals or any other contamination.