Tender Specifications AVK Surface box M-4055 MD-GG [80/30-011]

1. Range

4055 / fixed height 305 mm / PA+

2. Product description

General

The surface box shall be for installation in roads, sidewalks or green zones to provide access to underground hydrants.

Basic design

The surface box design shall correspond with AVK surface box M-4055 MD-GG series 80 type 30 variant 011 (STV 80/30-011) or equivalent.

Product shall be a heat resistant, synthetic surface box with a cast iron GJL-200 lid attached to the housing by a stainless steel A2-70 bolt with locking clip.

Housing shall consist of one part made out of heat resistant PA+ material.

Features

Surface box shall have a max. total weight of 11 Kg.

Housing shall be 100% corrosion-free.

Housing and lid shall be designed to ensure easy opening at all times

Surface box housing and lid shall have a heat resistance of at least 250 °C.

Surface box shall meet B125 load bearing capacity, tested by applying flat load on top surface.

Housing shall be equipped with vertical and horizontal ribs for optimal fixation in road.

3. Standards and approvals

Surface box design shall be derived from DVGW DIN 4055.

Surface box shall tested according to DVGW VP310-2 requirements.

4. Sustainability

Surface box shall have a carbon footprint of max. 19 Kg. Carbon footprint (CO2 emission) shall be calculated by using Lifecycle Assessment method according to ISO 14040-44. 
Housing to be made of 100% first grind recycled thermoplastic material.

Housing and lid to be 100% recyclable after end of life.

Surface box shall contain no heavy metals or any other contamination.